## Slide 1: smith to the rescue Saied Seghatoleslami ad2cc
July 22, 2023

## Slide 2: Not the one who went to Washington

## Slide 3: …AND Not agent smith

## Slide 4: … Phillip smith
Born April 29, 1905 in Lexington, MA
Died August 29, 1987 in Berkley Heights, NJ
Graduated from Tufts Collage in 1928
Retired from Bell Telephone Laboratories 1970
Elected Fellow of IRE 1952
Book published in 1969 “Electronic Applications of the Smith Chart: In Waveguide, Circuit, and Component Analysis”
Smith explained, "From the time I could operate a slide rule, I've been interested in graphical representations of mathematical relationships."

## Slide 5: Objectives
Understand why we care about Smith Charts
Look at some real-life antennas and see that they are not “just a resistor”
Stare at a Smith Chart (individual copies) and explore what is in there
Review some Smith Chart recipes
Solve a few problems using a Smith Chart
Look at one other use of a Smith Chart (RF Transistor data sheet)

## Slide 6: So, What does it do?
Smith Chart Takes the Drudgery Out of Radio Frequency (RF) Circuit Calculations
For Different Kinds of Antennas, RF Circuits, Transmission Lines…

## Slide 7: Why smith charts?
The alternatives are:
  Tedious and error prone (i.e., drudgery)
  Provide very little insights or help with intuition
What about computers?
  They take the tedium out
  But they give you even less insight
Smith Charts
  Simplify the task
  Give you insights and intuition about what is going on
  …and you can do Smith Charts with computers

## Slide 8: R, L, and C
Resistor – put a voltage across it, get a current through it
Capacitor, not so simple – put a voltage across it, you must ask what what is the frequency?
Inductors are also complicated – put a voltage across it, you must ask what what is the frequency?
Capacitor: The higher the frequency and the higher the capacitance, the lower the reactance (which is like resistance)
Inductor: The higher the frequency and the higher the inductance, the higher the reactance
R: resistance
X: reactance

## Slide 9
360o
90o

## Slide 10: …reactance has “phase”
x
y
Voltage
Capacitor current
Inductor current
x
y
X capacitive
Resistor current
X Inductive
R
Z

## Slide 11: Series circuits

## Slide 12: Parallel circuits

## Slide 13: Parallel World

## Slide 14: Real life antennas

## Slide 16: Two of my antennas
40 m
15 m

## Slide 17: Some of My antennas
40 m
20 m
15 m

## Slide 18: The math can get ugly
z
…Not so simple…Smith Charts to the rescue
z

## Slide 19: A few definitions
Transmission line with impedance of
Smith Chart is a plat of the reflection coefficient as a function of normalized resistance and reactance
(and normalized admittance and susceptance)

## Slide 20
Hand Out Smith Chart Paper

## Slide 21: Let’s look at a Smith Chart
Red circles are for resistance, red arcs are for reactance
Inductive reactance above the horizontal axis (positive)
Capacitive reactance below the horizontal axis (negative)
Resistance and reactance help when we put elements in series
On red resistance lines, rotate clockwise to add more inductance, counterclockwise to add more capacitance
The r = 1 circle signifies 50 ohms resistance (pure or in series with a reactance)
Horizontal line through the center is pure resistance

## Slide 22: SWR
The vector from the origin to a point on the chart is reflection coefficient of that point
Magnitude of the reflection coefficient is the length of the vector
Phase of the reflection coefficient is angle of the vector to the x axis
We can read the SWR from the scale on the bottom of the page since:

## Slide 23
You don’t have to remember the content of the last page,
it’s written on the Smith Chart

## Slide 24: Let’s work out an example
My 40 meter antenna on top of the band (7.3 MHz) looks like a 56.2 Ohms resistor in series with a 26 Ohms (839 pF) capacitive reactance
First, we normalize these values:
Then we find the point for this value on the Smith Chart using the red part (lower half of the chart since it is capacitive)
Now let’s add a 1,134 nH inductor in series with it:
  First calculate the reactance of the inductor at 7.3 MHz
  Then normalize it to 50 ohms
  And travel by that amount on the constant resistance circle (since we are not changing the resistance)
How did the SWR change?

## Slide 26: Let’s Find a (rough) match
A simple one component solution to get close to a match
Will it be an inductor or capacitor?
What is the best SWR we can achieve?
We need to move from a capacitive reactance of 0.52 to zero reactance
We need an inductance of the same and opposite value to resonate it out

## Slide 27: Let’s look at a Smith Chart
Blue circles are for conductance g (1/resistance) and blue arcs are for susceptance b (1/reactance)
Capacitive susceptance above the horizontal axis (positive)
Inductive susceptance below the horizontal axis (negative)
Conductance and susceptance help when we put elements in parallel
On blue lines, rotate clockwise to get more capacitance, counterclockwise for more inductance
The g = 1 circle signifies 1/50 ohms conductance (pure or in series with a reactance)
Horizontal line through the center is pure conductance

## Slide 28: Let’s work out an example
My 15 meter antenna on top of the band (21.45 MHz) looks like a 23.3 Ohms resistor in series with a 12 Ohms inductive reactance
First, we normalize these values:
Then we find the point for this value on the Smith Chart using the red part (upper half of the chart since it is inductive)
Now let’s add a 97 nH inductor in series with it:
  First calculate the reactance of the inductor at 21.45 MHz
  Then normalize it to 50 ohms
  And travel by that amount on the constant resistance circle (since we are not changing the resistance)

## Slide 29: Let’s work out an example
Now let’s add a 353 nF capacitor in parallel with it:
  First calculate the reactance of the capacitor at 21.45 MHz
  Then normalize it to 50 ohms
  Calculate susceptance (1/reactance)
  And travel by that amount on the constant conductance circle (since we are not changing the resistance)
How did the SWR change?

## Slide 31: Let’s find the equivalent circuit
All values are normalized to the system impedance

## Slide 33: A transistor

## Slide 35: Some of My antennas
40 m
20 m
15 m

## Slide 36
Discussion

## Slide 38: Quality Factor: Q
Parallel Circuit
If we want a C or L, then the resister in parallel with it is superfluous
The lower the resistor value, the more it interferes with the C or L
It lowers the “quality” of the circuit.
“Quality” is related to power dissipation which makes the part non-ideal
Q of a parallel circuit:
If we want an L or C, then the resister in series with it is superfluous
The higher the resistor value, the more it interferes with the C or L
It lowers the “quality” of the circuit.
“Quality” is related to power dissipation which makes the part non-ideal
Q of a series circuit
Series Circuit

## Slide 39: Parallel to series transformation

## Slide 40: Solve this with smith chart
Antenna is not 50 ohms (say it is 200 ohms)
Add capacitor in parallel
Use parallel to series conversion to see the result
Cancel out the capacitor with an inductor

## Slide 41: Match 70 ohms + 280 pF to 50 Ohms at 14.2 MHz
Calculate the reactance of the 280pF capacitor at 14.2 MHz: - 40 ohms
Normalize R and X to 50 ohms
r = 1.4 and x = - 0.8
Locate the point on the Smith Chart
Distance of this point to the origin is
Lay it out on the SWR scale and we get 2.2
This point is on the susceptance arc of 0.3
We need to get to the r=1 circle
Point 2 sits on the susceptance arc of 0.5
We need to add a susceptance of -0.5 – (- 0.3) = -0.2
We need to add a reactance of -1/0.2 or -5
-5 x 50 ohms = -250 ohms or 45 pf in parallel with the load
Point 2 sits on the reactance arc of -0.9
So, we add a reactance of 0.9 or 45 ohms in series
Which is 505 nH at 14.2 MHz

## Slide 42
n002

## Slide 43
40 m
20 m
15 m

## Slide 44: Recall Antenna Tuner Magic
Antenna is not 50 ohms (say it is 200 ohms)
Add capacitor in parallel
Use parallel to series conversion to see the result
Cancel out the capacitor with an inductor

## Slide 45: Resistance Transformation*
Example: 200 ohms load, want to match 50 ohms at 14.2 MHz (SWR = 4)
Recall:
Also recall:
*The math is in the last page

## Slide 46: Two Equivalent circuits
Recall:
Also recall:
We have the 50 ohms now, but what are we going to do with the C
We will resonate it out with an inductor with the same reactance
Recall:
These two circuits are equivalent

## Slide 47: Resonant Circuits cancel out
…And we have an antenna tuner that matches a 200 ohms load to a 50 ohms source
These two circuits are equivalent
The series inductance and series capacitance are in resonance with each other
These two circuits are equivalent